Water Quality Objective Monitoring, Indian River Watershed, 2013

Hydrologic and Geomorphic Characteristics of the Indian River Drainage Basin

The Indian River, a major tributary to the Yukon River, drains an area of approximately 2220 square kilometers and has an overall channel length of approximately 120 km.  The drainage basin is located 60 km south of Dawson.

Indian River, a gravel bed stream, is a tributary of Yukon River. The Indian River basin lies within the Klondike Plateau, a gently sloping upland south of Tintina Trench consisting of accordant summits (e.g., King Solomon Dome, Australia Mountain). The present flood plain descends about 53 m over a distance of 33 km with an overall gradient of about 1.6 m/km between the confluences of Dominion Creek and Ruby Creek.

The Water Survey of Canada (WSC) gauging station (09EB003) is located 1.5 km from the confluence of the Indian River with the Yukon River.

Topographical drainage Basin		2220 Sq. Kilometers

Area of Lakes					0%

Area of Forest					85%

Channel Length				120 Kilometers

Terrain						non-glaciated

In 2013, water samples were collected at 7 different sites in the Indian River basin.  Sampling commenced on July 4th, 2013 and a total of 143 samples were collected up until the end of the season on September 29th, 2013.  A combination of automatic composite sampling and grab sampling methods were used in the basin.

Atmospheric data was collected using two portable weather stations; one located near the mouth of the Indian River, the second at a background site on the Indian River.

Basin total flow data was provided to us by the Water Survey of Canada station located near the mouth of the Indian River.  Flow data for the individual tributaries to the Indian River was collected at the time of sampling by the staff of E.M.R CS&I using the methodology outlined in the Yukon Placer Secretariats, Water Quality Monitoring Protocol.

Site Codes and Global Position of Water Quality Sampling Locations in the Indian River Watershed

Water Quality Objective monitoring, Indian River Watershed – Summary

This basin has been extensively monitored for the past 10 years by many different organisations providing us with an immense amount of information regarding the state of the water quality in a historically mined watershed.  The Indian River basin is a heavily diverse watershed, with vast areas of active mining as well as inactive, reclaimed and partially reclaimed, sections.  Placer activities in this watershed have remained consistent over the last decade.

Two automatic water sampling station and two weather stations were set up and maintained from July 4th, until shutdown on September 29th, 2013.  From the data obtained by these instruments and through on site visits and sampling conducted by CS&I staff, the following observations regarding the water quality in the basin can be made:

The overall water quality in the basin, met the minimum objectives set under the Fish Habitat Management System throughout the monitoring season.  On average, the Total Suspended Solids concentrations, from water samples collected at our water quality monitoring sites was below 100 mg/L TSS.  The average TSS at the mouth of the Indian River was 73.3 mg/L in 2013 compared to an average of 75.3 mg/L in 2010, when we last had automated sampling equipment installed to monitor the watershed.

Low stream flows resulted in less suspension / re-suspension of sediment in the water.  Average seasonal rainfall led to only a slight increase in the amount of additional sediment entering the watercourse through runoff.  This in conjunction with already reduced effluent discharge volumes and effluent sediment concentrations improved the overall water quality in the Indian River watershed for 2013.