Water Quality Objective Monitoring, Klondike River Basin, 2011

Hydrologic and Geomorphic Characteristics of the Klondike River Drainage Basin

The Klondike River, a major tributary to the Yukon River, drains an area of approximately 7800 square kilometers and has an overall channel length, including the North Klondike River, of approximately 160 Km.

The North Klondike River, a tributary of the Klondike River, drains an area of approximately 1100 square kilometers.  From its headwaters in the Ogilvie Mountains, the North Klondike flows in a southerly direction for approximately 75 kilometers until its confluence with the Klondike.  It then flows west, down the valley as the Klondike for approximately 42 kilometers until it joins the Yukon River near Dawson.

The North Klondike, for its first 58 kilometers, flows through a narrow valley entrenched between high mountains, the remaining length of the Klondike River flows south through relatively flat topography.  The banks of the river are stable with relatively little erosion except during flood periods.

Water Survey of Canada’s gauging stations are located near the mouth of the North Klondike (09EA004, Km 9.5 Dempster Highway), and at the mouth of the Klondike River (09EA003) near Dawson.

North Klondike

Topographical drainage Basin		1100 Sq. Kilometers

Area of Lakes					<2%

Area of Forest					<44%

Channel Length				76.5 Kilometers

Terrain						glaciated

Klondike

Topographical drainage Basin		7800 Sq. Kilometers

Area of Lakes					<1%

Area of Forest					<30%

Channel Length				160 Kilometers

Terrain						Left Limit: non-glaciated

Right Limit: glaciated

In 2011, water samples were collected at 29 sites in the Klondike River basin, 13 more sites than in 2010.  Sampling commenced on May 24th, 2011 and 933 samples were collected up until the end of the season on September 29th, 2011, compared to the 406 samples that were collected in 2010.  A combination of automatic composite sampling and grab sampling methods were used in the basin.

Atmospheric data was collected using two portable weather stations, one located near the mouth of Bonanza Creek, the other at the North Klondike Fork.  Additional information was provided through the Yukon Government Community Services weather station at the Klondike Fire Center, located at the Dawson City Airport.

Blitz sampling events took place in the Klondike River basin on May 18thth, June 21st & 22nd , August 10th &30th and September 30th 2011.

Basin total flow data was provided to us by the Water Survey of Canada station located near the mouth of the Klondike River and .  Flow data for the individual tributaries to the Klondike River was collected at the time of sampling by the staff of E.M.R CS&I using the methodology outlined in the Yukon Placer Secretariats, Water Quality Monitoring Protocol.

Site Codes and Global Position of Water Quality Sampling Locations in the Klondike River Watershed

Water Quality Objective monitoring, Klondike River Watershed – Summary

Because of extensive monitoring activities conducted in this watershed between 2004 and 2010, which provided vast amounts of data for comparative purposes, and due to a large number of both active and historic mines in the drainage area, the Klondike River Watershed was once again designated a ‘major’ watershed for monitoring in 2011.

Nine automatic water sampling stations were set up and maintained from May 18th 2011 until shutdown on September 24th 2011, compared to the four automatic stations set up in 2010.  Four portable weather monitoring stations were used in both seasons (2010 and 2011).  Water sampling sites in the Klondike received multiple visits during the monitoring season due to their close proximity to Dawson.

From the data obtained by these instruments and through on site visits and sampling conducted by CS&I staff, the following observations regarding the water quality in the basin can be made:

On average, the water quality of the Klondike River, met the minimum objectives set under the Fish Habitat Management System throughout the monitoring season.  On those occasions when the WQO were not met and the Total Suspended Solids levels were greater than the objectives, a direct correlation between environmental conditions and the volume of solids in the water was observed.

In most cases, rainfall, as either localised events or basin wide occurrences, increased the amount of surface run off and subsequent soil erosion from the land, increasing the input of sediment into the receiving waters.  These increases occurred simultaneously at the time of the rain event or immediately in a period of one or two days after the rain event, as surface water continued draining from the land and ground water infiltrated the watercourse.

Increases in sediment-laden ground and surface water entering the system add to the amount of sediment in the water.  The ability of the receiving water to dilute these inputs of sediment is negated by the re-suspension of streambed material and by the further erosion of the streams banks that occurs along with the increased flows that are generated by the aftermath of these rain events.

All of these factors; precipitation leading to increased sediment input and increased flows from these rain events re-suspending and further eroding material, lead to an increase in suspended solids concentrations in 2011 when compared with the results from 2010 and a decrease in overall water quality.  The seasonal average TSS for 2011 was 24 mg/L which is approximately 18 mg/L higher than in 2009 (5.7 mg/L) and 124% higher than the 10.8 mg/L average in 2010.

However, it is important to note that the average water quality of the Klondike River at site KL03, which is up stream of the major discharge of Hunker and Bonanza Creeks, both areas of significant previous development, was 42.4 mg/L, 17 mg/L higher than the water quality objective of 25 mg/L.  This is a direct result of increased surface water runoff and increased ground water infiltration.  This in due in part to above average seasonal rainfall and higher than average seasonal air temperatures which resulted in more saturated ground, warmer ground temperatures and a greater degradation of the permafrost.

# Text boxes

Site Code

Alias

Location

Latitude

Longitude

KL01

K 01

Klondike River mouth

64.053480

-139.439610

KL02

K 02

Klondike River upstream of Bonanza Creek

64.043110

-139.409360

KL03

K 03

Klondike River at Marcels Sauna

64.047050

-139.126740

KL04

K 04

Klondike River downstream of Goring Creek and upstream of Hunker Creek

64.058100

-139.030917

KL05

K 05

Klondike River at Dempster Highway

63.990300

-138.746120

KL06

K 06

Klondike River downstream of Too Much Gold Creek and upstream of Dempster highway

63.957776

-138.690301

KL07

K 07

Klondike River upstream of Too Much Gold Creek

63.951313

-138.666902

KL08

K 08

Klondike River at highway washout downstream of Flat Creek

63.957817

-138.690050

KL_NK01

KN 01

North Klondike River upstream of confluence with Klondike River

64.001950

-138.596220

KL_BO_AD01

K ADAM 01

Adams Creek mouth

63.934120

-139.330990

KL_AL01

K ALLG 01

All Gold Creek below all mining

63.942630

-138.617340

KL_BO_EL01

K ELDO 01

Eldorado Creek mouth

63.919430

-139.313900

KL_BO_EL06

K ELDO 01A

Eldorado Creek Left Fork

63.862610

-139.245730

KL_BO_EL05

K ELDO 01B

Eldorado Creek Right Fork

63.862610

-139.245730

KL_BO_EL02

K ELDO 02

Eldorado Creek downstream of French Gulch

63.912670

-139.314830

KL_BO_EL03

K ELDO 03

Eldorado Creek upstream of French Creek

63.908550

-139.313817

KL_BO_EL04

K ELDO 04

Upper Eldorado Creek background

63.861867

-139.245783

KL_FL01

K FLAT 01

Flat Creek below all mining

63.943080

-138.602250

KL_BO_EL_FR01

K FREN 01

French Gulch mouth

63.908650

-139.314417

KL_HU_GO01

K GOLDB 01

Gold bottom Creek mouth

63.964330

-138.967060

KL_HU_LA01

K LAST 01

Last Chance Creek mouth

64.010500

-139.090910

KL_TO01

K TOO 01

Too Much Gold Creek mouth

63.951317

-138.667083

KL_BO_VI01

K VIC 01

Victoria Gulch mouth

63.912610

-139.209300

KL_BO01

KB 01

Bonanza Creek below all mining

64.040540

-139.408140

KL_BO02

KB 02

Lower Bonanza Creek

64.012950

-139.370217

KL_BO03

KB 03

Lower Bonanza Creek downstream of bridge

63.970267

-139.354717

KL_BO04

KB 04

Bonanza Creek downstream of Adams Gulch

63.935500

-139.327983

KL_BO05

KB 05

Bonanza Creek upstream of Adams Gulch

63.934150

-139.329770

KL_BO06

KB 07

Bonanza Creek downstream of Eldorado Creek

63.920467

-139.316000

KL_BO07

KB 08

Upper Bonanza Creek upstream of Eldorado Creek

63.919430

-139.313900

KL_BO08

KB 09

Upper Bonanza Creek upstream of Victoria Gulch

63.912610

-139.209300

KL_HU01

KH 01

Hunker Creek below all mining

64.029430

-139.178670

KL_HU02

KH 02

Hunker Creek downstream of Henry Gulch

64.028383

-139.175217

KL_HU03

KH 04

Hunker Creek downstream of Last Chance Creek

64.013450

-139.091870

KL_HU04

KH 05

Hunker Creek upstream of Last Chance Creek

64.010500

-139.090910

KL_HU05

KH 06

Hunker Creek downstream of Gold bottom Creek

63.968800

-138.982240

KL_HU06

KH 08

Hunker Creek upstream of Gold bottom Creek

64.964330

-138.967060

KL_HU07

KH 09

Hunker Creek above all mining left fork

63.911050

-138.885217

KL_HU08

KH 10

Hunker Creek right fork

63.890250

-138.925217

KL_HU09

KH 11

Hunker Creek above all mining and downstream of right and left fork

63.915030

-138.885010