Water Quality Objective Monitoring, Yukon River North , 2010

Hydrologic and Geomorphic Characteristics of the Yukon River North Watershed

The Yukon River is a major watercourse of north western North America.  Over half of the river lies in the U.S. state of Alaska, with most of the other portion lying in and giving its name to Canada's Yukon Territory, and a small part of the river starts near the rivers source in British Columbia.  The river is 3,700 km long and empties into the Bering Sea at the Yukon-Kuskokwim Delta.  The average flow is 6,430 m³/s.  The total drainage area is 832,700 km² of which 323,800 km² is in Canada.  By comparison, the total area is more than 25% larger than the province of Alberta.

The Yukon River is divided into two sections, the North Yukon section, downstream from the Yukon Rivers confluence with the White River and the South Yukon, the section of the Yukon River upstream from its confluence with the White River.  The average water quality of the North Yukon River is much more turbid and higher in suspended solids concentrations than that of the South Yukon due to the huge contribution of sediment and glacial material entering the Yukon River from the White River drainage.  Total suspended solids concentrations in the North Yukon can be 10-25 times higher than those found in the South Yukon.  Many large tributary rivers and streams flow into the catchment area of the Yukon River basin.

In 2010, 149 grab samples were taken by inspection staff on behalf of the Water Quality Team at 54 different locations in the Yukon River North basin.  Basin total flow data was provided to us by the Water Survey of Canada station located on the Yukon River above the White River.

Yukon River North Placer Authorization

On April 11, 2008, pursuant to Section 35(2) of the Federal Fisheries Act; The Minister of Fisheries and Oceans Canada revoked the conditions of the Yukon Placer Authorization (issued June 1993) and all subsequent amendments pertaining to placer mining works or undertakings and sediment discharge standards in the Yukon River North watershed.

The Minister then authorized the “harmful alteration, disruption or destruction of fish habitat” resulting from placer mining works or undertakings and the discharge of sediment at concentrations specified in the new authorization, which are uncontaminated by deleterious substances, within certain streams or portions of streams in the Yukon River North watershed.  The areas of allowable discharge are identified on the Yukon Placer Fish Habitat Suitability Map for the Yukon River North watershed (Schedule 1) and the sediment discharge standards for mine discharge (allowable sediment discharge concentrations) detailed in the Sediment Discharge Standards for Placer Mine Effluent – Yukon River North watershed (Schedule 2).

Under these new authorizations, it was decided to incorporate a 3 year phase-in schedule for the sediment discharge standards that would apply to each Placer mining operation in the Yukon.  This phase-in period would allow both the government mining inspectors and the Yukon Placer Secretariat enough time to ensure that each operator fully understood their requirements to comply with the new authorizations and to operate within the framework of the new management system for Placer mining in the Yukon.  The 3 year phase-in schedule contains the following requirements:

In 2008 – Licensed placer miners would be informed about the operating practices required to comply with the new system for managing placer mining activity under the Fisheries Act. Inspectors and the Yukon Placer Secretariat would ensure that each operator is aware of the specific changes required at his or her site.

In 2009 – All licensed placer miners must be oriented to the Design Target and Action Level detailed within the authorization pertaining to the watershed they are operating in and, must comply with a Sediment Discharge Standard for Mine discharge of no greater than 2.5 ml/L, or the standard stipulated in their existing water use license, whichever is more stringent.

And in 2010 – All operations must be oriented to operate within the Design Target and Action Level, and must not exceed the Compliance Level stipulated in the table of Sediment Discharge Standards for Placer Mine Effluent (Schedule 2) for the habitat suitability classification and the watershed in which the mine is located.

Highly sensitive habitat received a high degree of protection under the YPA, and that is maintained in the new system. The degree of disturbance of all mined tributaries in each watershed is recognized under the new rules by the Previous Development designation.  The Water Quality Objectives and related discharge standards that are set are designed to mitigate the potentially negative downstream effects of placer mining.

High suitability habitats (Areas of Special Consideration) are defined as watercourses that contain ecologically or culturally important fisheries or aquatic resources.  Watercourses assigned this designation may include habitats for rare or locally significant species or areas which directly support subsistence, traditional, commercial or sport fisheries.  Areas of Special Consideration (ASC) may be established for either anadromous or nonanadromous species of fish.

In all cases, any placer mining activities that are likely to result in the harmful alteration, disruption or destruction of High (ASC) suitability habitats require a site-specific review, and if the activity is deemed to be acceptable, a site-specific authorization issued by Fisheries and Oceans Canada.  In order to further protect these ASCs, a full compensation and fish habitat restoration plan must be submitted to Fisheries and Oceans Canada with any proposal to conduct works in or around High (ASC) suitability habitats.

In moderately sensitive habitat where mining has occurred for decades, the Previous Development designation results in application of a less stringent discharge standard, recognizing that the habitat features predicted by the classification model likely do not exist.

Site Codes and Global Position of Water Quality Sampling Locations in the Yukon River North Watershed

Water Quality Objective monitoring, Yukon River North Watershed – Summary

On those occasions when the WQO were not met and the Total Suspended Solids levels were greater than the objectives, there is a direct correlation to environmental conditions influencing the amount of solids concentrations in the water.

As noted above, the Yukon River is divided into the North and South Yukon River at its confluence with the White River.  The water quality of the North Yukon River is heavily influenced by the sediment rich meltwater that enters the Yukon River from the discharge of the White River.  The huge amount of glacial sediment that enters the Yukon River from the White degrades the water quality of the Yukon beyond the river’s ability to dilute the sediment load to a level of compliance.  The Yukon River North remains heavily turbid all the way until its confluence with the Arctic Ocean.

Beginning in mid May, and peaking in mid June, the seasonal ‘spring’ freshet increases the flow of the Yukon River and helps to dilute the flow from the White River.  By the beginning of August, the flow of the Yukon River is usually at its lowest level while the White River continues to input a continuously even flow of sediment into the receiving waters of the Yukon, all the way until the end of August.  The water quality of the Yukon River is generally at its lowest during this August period until the flow of the White River begins to subside, and clean water inputs to the Yukon River increase.

Throughout the season, rain fall, either as localised events or basin wide occurrences, increase the amount of surface water run off and the volume of stream flows in the basin.  Increases in sediment laden ground and surface water entering the system can add to the amount of sediment in the water.  The ability of the receiving water to dilute these contributions of sediment is negated by the re-suspension of stream bed material and by the further erosion of the streams banks that occurs along with the increased flows that are generated by the aftermath of these rain events.

All of these factors; vast amounts of meltwater entering the system, precipitation leading to increased sediment input and increased flows re-suspending settled material and further eroding stream and river banks, lead to an increase in suspended solids concentrations and a decrease in water quality.